**********************Default**********************
Programming Pico with Ardiuno IDE
for Nano-RP2040-Connect
Ultra Sonic sensor with PIO

generating trigger
and receiving echo
and a 2nd version using pico-sdk
10/18/22
**********************Default**********************

Pico

Ultrasonic sensor

diff --git a/CMakeLists.txt b/CMakeLists.txt
index 5fbbfb3..e255b4d 100644
--- a/CMakeLists.txt
+++ b/CMakeLists.txt
@@ -22,6 +22,7 @@ add_subdirectory(Semaphore)
 add_subdirectory(Mutex)
 add_subdirectory(Scheduling)
 add_subdirectory(first_pwm)
+add_subdirectory(HCSR04)^M
 add_subdirectory(2tasks)
 add_subdirectory(ultibo_blink)
 add_subdirectory(pico-lifting-sf)

export PICO_SDK_PATH=../pico-sdk/

make

 openocd -f interface/raspberrypi-swd.cfg -f target/rp2040.cfg -c "program HCSR04/HCSR04.elf verify reset exit"

A 2nd source code was used from https://github.com/GitJer/Some_RPI-Pico_stuff..
Minor changes were required to 2 files CmakeLists.txt & HCSR04.cpp.

HCSR04.cpp
86,87c86,87
< // the instance of the HCSR04 (Echo pin = 4, Trig pin = 7)
< HCSR04 my_HCSR04(4, 7);
---
> // the instance of the HCSR04 (Echo pin = 14, Trig pin = 15)
> HCSR04 my_HCSR04(14, 15);
94c94
< sleep_ms(1000);
---
> sleep_ms(100);
96c96
< }
---
> }
\ No newline at end of file
CMakeLists.txt
13,14c13
< pico_enable_stdio_usb(HCSR04 1)
< pico_enable_stdio_uart(HCSR04 0)
---
>
16c15
< #example_auto_set_url(HCSR04)
---
> example_auto_set_url(HCSR04)

I used 5 volts from the pico to power the HCSR05. This required using 2 10K ohm resistors on the echo signal.

This was the origin of this project. https://github.com/develone/my-projects-docs/blob/master/HCSR04/ultrasonic-sonar-distance-sensors.pdf

This is sensor sending data over the USB to a serial terminal.

Arduino Library Manager

Github

https://github.com/MrYsLab/NanoConnectHcSr04/blob/master/src/NanoConnectHcSr04.pio.h

https://github.com/MrYsLab/NanoConnectHcSr04/blob/master/src/NanoConnectHcSr04.cpp

This sketch uses NanoConnectHcSr04 library

For the pico gpio 7 is pin 10 gpio 4 is pin 6

For the nano-rp2040-connect gpio 7 is pin 12 gpio 4 is pin 11

Serial Port configuration